## Slide 1
DFT Software – Free version
  ELKFP-LAPW code
  USPEX
  CASTEP (command mode free with in UK. I had that pirated version is available. But, i don’t have.)
  ABNIT
  Quantum espresso
CALPHAD – Free version
  OpenCalphad (OC)

## Slide 2: Thermodynamic Reassessment of Ni-Ti-Zr sytem by coupling CALPHAD approach with Density Funcitional Calculations
This system has two ternary compounds.
Thermodynamic assessment Ni-Ti-Zr system was completed already in 2007. The author considered only one ternary compound in their assessment with the help of DFT.
Possibilities:
  Identify the phase stability of that ternary phase using DFT
  Calculate the end member energy using DFT
  Incorporate those phase in Ni-Ti-Zr system assessement using CALPHAD approach.

## Slide 3: Thermodynamic reassessment of Mg-Sr-Zn system
There are 4 ternary compounds present in Mg-Sr-Zn system.
Thermodynamic assessment of Mg-Sr-Zn system is completed considering one ternary compound.
Thermodynamic reassessment can be done for this system by incorporating remaining ternary compounds using CALPHAD approach.

## Slide 4: Phase stability of Mg-Sr-Zn ternary compounds using DFT
There are four ternary compounds in Mg-Sr-Zn system.
Crystal structure of one ternary compound is already identified by experimentally.
Remaining ternary compounds crystal structure has to be identified using similar kind of systems like Mg-Ca-Zn, Mg-Nd-Zn.
Using DFT, identify the heat of mixing for their stability.

## Slide 5: Crystal structure identification of Ni3(Ti0.7V0.3)
Ternary compound Ni3(Ti0.7V0.3) occurs in rhombohedral structure (R phase) at low temperature and DO19 structure at high temperature.
Low temperature phase of Ni3(Ti0.7V0.3) is experimentally identified and reported in 1984.
In 2002, another author reported Ni3Ti-Ni3V isothermal section in which mentioned low and high temperature phases of Ni3(Ti0.7V0.3). The author most probably presented in conference which is not published. But in Al-Ni-Ti-V system, the same isothermal sections are used.
Possibility for present work
  Ni3(Ti0.7V0.3) alloy available which is heat treated at 900 and 1000C. The formation of R phase and DO19 are sluggish. Hence microstructures are not formed.
  XRD results shows Ni3(Ti0.7V0.3) alloy has combination of Ni3V and N3Ti structures.
  It has to be further heat treated for long time to obtain the R and DO19 phase.
  Has to be characterized with the help of SEM, XRD and DTA.